Edinburgh & Lothians Miniature Railway Club

Schmalzberg.

Club Contact Details

This layout is privately owned by a member of the club.

Website www.elmrc.org.uk

Email: secretary@elmrc.org.uk

Exhibiting:

The layout and operators can be transported in one car plus trailer.

Setting up or dismantling the layout takes around an hour.

We can supply barriers; please let us know if you require us to provide them.

The layout is equipped with lighting.

Layout Details:

Scale 3.5mm/ft - H0e

Layout Size = Size 2.44m (8') x 0.6m (2') including the swing of the storage yard turntable, but excluding barriers and operating space. Please allow 4 feet operating space along the back of the layout. We prefer a minimum of 2 feet between the layout and barriers. Please allow operator access to one end or back of the layout.

Operated: From rear, number of operating positions 1.

Short Description:

Schmalzberg. 3.5mm/ft Narrow Gauge 'HOe'. Period late 1990s. The layout represents a German preserved narrow gauge railway.

Full Description

The Prototype

Unlike in Wales where most narrow gauge railway were built to serve a single industry, in Germany they are more like secondary railways serving the general traffic of the area in the manner of branch lines in this country. Similar lines were built in Britain, the Welshpool & Llanfair or the Lynton & Barnstaple being examples.

On Continental narrow gauge lines the goods traffic is usually handled by loading the standard gauge wagons onto transporter wagons known as ‘Rollwagon’ rather than by transhipping between wagons.

The Model

Schmalzberg is a freelance model representing a German narrow gauge 'Museumsbahn' (preserved railway). While it has no particular prototype the idea is loosely based on Germany’s first preserved railway, the DEV (Deutscher Eisenbahn-Verein e.V), which is situated south of Bremen. Some features are taken from other narrow gauge railways; street running is a feature of the Bad Doberan line near Rostock.

The main line runs to the front of the layout before entering the station. Behind the passenger station lies the goods yard containing the ‘Rollwagen’ loading point. The station is also the junction for a branch that leaves the town via one the streets.

Locomotives are mostly built from kits with a couple of ready to run models, while coaches and wagons are all ready to run.

The buildings are made from plastic kits from various manufacturers.

Track Plan

The track plan is available as a 300dpi jpg file